## Slide 1
Wearable sEMG fatigue monitoring on roofers in hot environment
Sujan Acharya and Krishna P. Kisi, Ph.D., P.E. · Texas State University
Nepali migrants build much of the Gulf, roofing through summer afternoons on short contracts, with musculoskeletal disorders carried home rather than recorded.
Muscle fatigue precedes those disorders and the falls that injure roofers. Surface EMG (sEMG) tracks fatigue as it builds, before a worker feels it, so a body-worn sensor could warn in time. Nearly all of that evidence comes from cool laboratories.
We ran one protocol twice: indoors on a 30° platform, then on a real roof at 37–39 °C. Nine of ten channels were usable indoors, four on the roof, and the model fell to 49%. Heat and sweat took the leg channels first, so placement decides whether a study measures fatigue or noise. Nepal builds the same roofs, with no field data of this kind.
Gulf towers
shift change in the heat
roof work at home
9
4
LABORATORY
REAL ROOF
sensor channels we could use
out of ten
2.3×
1.3×
LABORATORY
REAL ROOF
signal working vs resting
higher is easier to read
9
19
LABORATORY
REAL ROOF
signal while resting
µV at the lower back
20
8
POSSIBLE
WE CAN READ
muscle-and-posture tests
kneeling and stooping
our roof platform
on the worker
the sensor itself
the field station
One session day: 32.8 °C through the morning block, 38.9 °C by five. NOAA station KHYI, San Marcos, 14 August 2025.
A channel counts only if it passes all three checks
1 Above the noise floor
bigger than the sensor's own 3–5 µV noise
2 Above its own rest
working signal beats the same channel at rest
3 In the muscle band
median frequency between 50 and 150 Hz
the same 30° platform, indoors
ten muscles, trunk to calf
Illustration (AI generated)
Why this happened
Sweat breaks the contact, so the signal gets smaller.
Heat and holding a posture lift the resting level.
Small muscles start closest to the noise, so they cross into it first.
Rest is no longer rest
19 µV on the roof against 9 µV in the lab.
Each dot is one worker.
Most comparisons are gone
the leg muscles that matter for balance are the ones we lost
The model inherits the damage
trained one worker at a time, it lands at 49% on roof data
Where Nepal starts
No roof-worn data exists there.
Trunk first
both sides of the lower back, plus one leg channel
Check the signal live
a dead channel cannot be fixed later
Teach it where workers train
vocational centres, pre-departure briefings
22 workers · 30° platform · one processing pipeline · every number here is computed from the recordings at print time · Limitation: different people in each setting, 13 in the laboratory and 9 on the roof, not the same workers tested twice
Reference: Acharya, S., Kisi, K., Gautam, S. R., Mahmud, T., & Kayastha, R. (2025). A high-performance hybrid transformer–LSTM–XGBoost model for sEMG-based fatigue detection in simulated roofing postures. Buildings, 15(17), 3005.
Gulf and Nepal photographs: Imre Solt (CC BY-SA 3.0) and Adam Jones (CC BY-SA 2.0), via Wikimedia Commons.
Sweat-on-the-electrode image: made with Google Flow (Nano Banana 2).
19th Annual ASNEngr Conference
Houston, Texas · November 21, 2026
1
Abstract
2
Methodology
In the laboratory
On a real roof mock-up in hot environment
13 laboratory participants · 9 roof workers · Texas State University IRB #9962
3
Results
4
Lessons Learned
5
Conclusion
Laboratory channel counts do not survive a hot roof: nine become four and accuracy falls to 49%. Validate on the roof, keep the trunk channels, and teach the check where workers train.